BrewBuddy: Overview
Author : Marcelo Barros de Almeida
Email : marcelobarrosalmeida@gmail.com
Project: https://hackaday.io/project/28667-brewbuddy
Code : https://github.com/marcelobarrosalmeida/brewbuddy

---
BrewBuddy: Thermometer
Author : Marcelo Barros de Almeida
Email : marcelobarrosalmeida@gmail.com
Project: https://hackaday.io/project/28667-brewbuddy
Code : https://github.com/marcelobarrosalmeida/brewbuddy

---
BrewBuddy: Moisture
Author : Marcelo Barros de Almeida
Email : marcelobarrosalmeida@gmail.com
Project: https://hackaday.io/project/28667-brewbuddy
Code : https://github.com/marcelobarrosalmeida/brewbuddy

---
BrewBuddy: Boiling/Hoping
Author : Marcelo Barros de Almeida
Email : marcelobarrosalmeida@gmail.com
Project: https://hackaday.io/project/28667-brewbuddy
Code : https://github.com/marcelobarrosalmeida/brewbuddy

---
What is BrewBuddy ?
BrewBuddy is a compact device for helping homebrewers in their exhausting task of converting malts, hops and yeasts into happiness !

---
BrewBuddy Functions
  - Thermometer: like an analog thermometer but aggregating time control via stopwatches (progressive and regressive).
  - Step mash: You can program your temperature steps and duration when mashing. BrewBuddy will blink a led when an step is finished.
  - Hop additions: When boiling, it is very easy to program your hop additions. Again, BrewBuddy will indicate when it occurs.

---
BrewBuddy Functions
  - You can program up to ten mesh steps and ten hop additions.
  - Your last setup is automatically saved in non volatile memory.
  - BrewBuddy is powered by a CR2032 battery, working up to 20 hours.
  - Menus and configurations are simple and intuitive, you will learn all function in minutes.

---
Main Components
  - Microcontrolled PCB using a low cost STM32F030F4
  - OLED Display 128x64
  - LMT86 analog temperature sensor
  - ADR5041BRTZ voltage reference (2.5V)
  - Stainless steel tube for temperature measurement
  - 3D housing under development

---
BrewBuddy Navigation
On/off in a
single button
Indication
led
UP button
RIGHT button
LEFT button
DOWN button

---
BrewBuddy Menu
BrewBuddy
starts here !
BOILING
MOISTURE
THERMOMETER
Boiling programming (temperature and duration).
Hop additions programming (duration).
Boiling/hops follow up.
Step programming (temperature and duration).
Steps follow up.
Temperature follow up and time measurements

---
Demonstration Video
For faster demonstration, usual timer (whose unit is minute) was replaced by a timer in seconds. Moreover, temperatures were simulated.
►Demonstration mode: turn BrewBuddy on with LEFT button pressed
►Factory init mode: turn BrewBuddy on with RIGHT button pressed